Changes to the Administration Rules

Administrative Rules

265:25-1-4 – Building permits – application – plans – construction or repair or alteration or change of use

- All use and occupancy classifications identified in the International Building Code and Specific Situations identified in the International Fire Code must have building plans submitted for review and be permitted by the Oklahoma State Fire Marshal’s Office.

- Any owner or owner’s authorized agent who intends to construct, enlarge, alter, repair, move, demolish or change the occupancy of a building or structures, or to erect, install, enlarge, alter, repair, remove, convert or replace any electrical, gas, mechanical, or plumbing systems, the installation of which is regulated by this code, or to cause any such work to be performed, shall first make application to the Oklahoma State Fire Marshal’s Office and obtain the required permit.

- Any change of ownership, change in occupancy use or classification, and/or the building has been unoccupied/vacated for at least 90 days involving any of the use and occupancy classifications identified in the International Building Code and Specific Situations identified in the International Fire Code must be brought up to current code requirements.

- All State owned or State occupied projects must be permitted by the Oklahoma State Fire Marshal’s Office.

- The Authority Having Jurisdiction (AHJ) hierarchy is as follows:

- Oklahoma State Fire Marshal – overseas the entire State of Oklahoma unless the County or City has provided the State Fire Marshal approved document, entirely filled out with no alterations, (AHJ letter) to the Oklahoma State Fire Marshal’s Office

- County – Assumes the responsibility from the Oklahoma State Fire Marshal’s Office and overseas the entire County within the State of Oklahoma and has provided the State Fire Marshal approved document, entirely filled out with no alterations, (AHJ letter) to the Oklahoma State Fire Marshal’s Office

- City-Assumes the responsibility from the Oklahoma State Fire Marshal’s Office and overseas the entire city limits within the State of Oklahoma and has provided the State Fire Marshal approved document, entirely filled out with no alterations, (AHJ letter) to the Oklahoma State Fire Marshal’s Office

- Subdivision-Assumes the responsibility from the Oklahoma State Fire Marshal’s Office and overseas the entire subdivision limits within the State of Oklahoma and has provided the State Fire Marshal approved document, entirely filled out with no alterations, (AHJ letter) to the Oklahoma State Fire Marshal’s Office

- All counties that take jurisdiction in writing (AHJ letter) to the Oklahoma State Fire Marshal’s Office must permit all project types identified on the Authority Having Jurisdiction letter within the Entire County of the State of Oklahoma in which is resides.

- Only a positive pressure primary water source and/or tanks can be used as a reliable primary water source.

  - No ponds

  - No pools

  - No open top containers

  - No cisterns

  - No similar sources as identified above

- All assembly and educational buildings/press boxes intended to have occupants on the roof is required to have a letter from the engineer confirming compliance in regards to the added roof load.  An occupant load sign shall be provided identifying the maximum occupant load based on the engineer’s roof load calculations.  Guards shall be installed around the areas with occupants and shall meet the requirements of the International Building Code Section 1015.  Two means of egress are required to provide access off the roof for the occupants.

265:25-1-5 – Carbon Dioxide

- All occupancies with a carbon dioxide system must have properly installed carbon dioxide detector(s).  If there is a fire alarm system installed the carbon dioxide detector(s) must be tied to the fire alarm system and sound a general alarm both in the audible and visual form.  If there is not a fire alarm system the carbon dioxide detector(s) must provide a local alarm both in the audible and visual form.  Plans must be submitted and reviewed by the Oklahoma State Fire Marshal’s Office.  All permitting requirements are identified on the Oklahoma State Fire Marshal’s Office website.  (NFPA 72)

265:25-1-6 – Smoke Detection

- All occupancies with a smoke detection system tied directly to the electrical system (as permitted by the International Building Code and the International Fire Code) and not tied to the fire alarm system must follow all the permitting requirements for a fire alarm system as identified on the Oklahoma State Fire Marshal’s website.  Plans must be submitted and reviewed by the Oklahoma State Fire Marshal’s Office.

265:25-1-7 – Access Control

- All occupancies with access controlled entrance and/or egress must first make contact with the appropriate fire alarm company to discuss proper connections.  Plans must be submitted and reviewed by the Oklahoma State Fire Marshal’s Office.  All permitting requirements are identified on the Oklahoma State Fire Marshal’s Office website.

265:25-1-8 – Smoke Control

- All occupancies with a smoke control system must first make contact with the appropriate fire alarm company and heating ventilation and air conditioning Company to discuss proper connections, activation, desired results.  Plans must be submitted and reviewed by the Oklahoma State Fire Marshal’s Office.  All permitting requirements are identified on the Oklahoma State Fire Marshal’s website.  (NFPA 92)

265:25-1-9 – Carbon Monoxide

- All occupancies with a carbon monoxide system must have properly installed carbon monoxide detector(s).  If there is a fire alarm system installed the carbon monoxide detector(s) must be tied to the fire alarm system and sound a general alarm both in the audible and visual form.  If there is not a fire alarm system the carbon monoxide detector(s) must provide a local alarm both in the audible and visual form.  Plans must be submitted and reviewed by the Oklahoma State Fire Marshal’s Office.  All permitting requirements are identified on the Oklahoma State Fire Marshal’s Office website.

265:25-1-10 - Inspections

- As referenced by the Oklahoma State Statute all Correctional facilities are required to be annually inspected by the Oklahoma State Fire Marshal’s Office.  The inspected will be based off NFPA 101-Life Safety Code.

- As referenced by the Oklahoma Department of Human Services, the Oklahoma State Fire Marshal’s Office is required to inspect all Day Care Facilities that fall under the Oklahoma State Fire Marshal’s jurisdiction.  The inspection will be based off NFPA 101-Life Safety Code.

- The Oklahoma State Fire Marshal’s Office performs an inspection of Education facilities up to the 12th grade that fall under the Oklahoma State Fire Marshal’s jurisdiction.  The inspection will be based off NFPA 101- Life Safety Code.

- As referenced by the Oklahoma Department of Health, the Oklahoma State Fire Marshal’s Office is required to annually inspect all Assisted Living Facilities that fall under the Oklahoma State Fire Marshal’s jurisdiction.  The inspection will be based off NFPA 101-Life Safety Code.

- The Oklahoma State Fire Marshal’s Office performs an inspection of State of Oklahoma state owned facilities or facilities rented by the State of Oklahoma.  The inspection will be based off NFPA 101-Life Safety Code.

- As referenced by the Horse Racing Commission all Race Tracks are required to be annually inspected by the Oklahoma State Fire Marshal’s Office.  The inspected will be based off NFPA 101-Life Safety Code.

- All educational facilities are required to have a commercial fire alarm system installed in accordance with NFPA 72.  The commercial fire alarm system shall be monitored by a central station.