## Slide 1
WELCOME
Virtual Open House Public Meeting
PROJECT
US-412A
from the US-412A / US-412 Junction to SH-10 Delaware County Job Piece 30373(04) & 30373(07)
July 27, 2023, to August 10, 2023
Notes: Welcome to the Virtual Open House Public Meeting for US-412A beginning at the US-412A / US-412 junction and extending east to State Highway 10 in Delaware County.
This presentation provides a review of the purpose of the virtual open house public meeting, the purpose and need for the project, the proposed improvements, and the environmental impacts.

## Slide 2
Purpose of the Virtual Open House Public Meeting
Inform the public about the proposed roadway improvements of US-412A from the US-412A / US-412 Junction to SH-10 (11.35 miles) in Delaware County.
2
Notes: The purpose of this virtual open house public meeting is to inform the public about the proposed improvements to US-412A from the US-412A / US-412 junction to State Highway 10 in Delaware County.
As noted on the map, two construction projects are programmed for the corridor.
The presentation summarizes the proposed design improvements, describes potential environmental impacts, explains how to ask questions or make comments on the project, and outlines the schedule for the project.

## Slide 3
Purpose of the Project
What are we trying to do?
1
Provide a Safety Improvement along US-412A
2
3
4
Improve the narrow highway and bridges
Improve highway geometry
Upgrade the roadway to meet current Federal Highway Administration (FHWA) and Oklahoma Department of Transportation (ODOT) design standards
Improve the skewed roadway intersection connections
Notes: What are we trying to do? The purpose of the project is to improve safety along US-412A by improving the narrow roadway and bridges, improving the roadway geometry, improving the skewed roadway intersection connections, and upgrading the roadway to meet current Federal Highway Administration (FHWA) and Oklahoma Department of Transportation (ODOT) design standards.

## Slide 4
Existing US-412A Highway
Existing Conditions
Existing highway
  Two 12-foot-wide driving lanes
  Varying 0 to 2-foot-wide paved shoulders
Notes: The existing highway consists of two 12-foot-wide driving lanes with shoulders varying from 0 to 2-foot-wide paved sections.

## Slide 5
Traffic Data
Current and Projected
JP 30373(04) Project | US-412A from US-412A / US-412 junction extend east 7.35 miles to SH-412A junction
  Current Traffic (2023)
    1,650 vehicles per day (US-412A / US-412 junction to S 530 RD)
    3,200 vehicles per day (S 530 RD to SH-412A junction)
  Projected Traffic (2047)
    2,100 vehicles per day (US-412A / US-412 junction to S 530 RD)
    4,000 vehicles per day (S 530 RD to SH-412A junction)
  5% of traffic is commercial trucks
JP 30373(07) Project | US-412A from US-412A / SH-412A junction extend east 4.0 miles to SH-10 junction
  Current Traffic (2023)
    6,350 vehicles per day
  Projected Traffic (2048)
    7,950 vehicles per day
  5% of traffic is commercial trucks
Notes: Current traffic (2023) in the Job Piece 30373(04) Project segment from US-412A / US-412 junction extending east 7.35 miles to State Highway 412A junction are 1,650 vehicles per day from the US-412A / US-412 junction to South 530 Road and 3,200 vehicles per day from South 530 Road to State Highway 412A. By 2047, traffic is expected to grow to 2,100 vehicles per day from the US-412A / US-412 junction to South 530 Road and 4,000 vehicles per day from South 530 Road to State Highway 412A.
Current traffic (2023) in the Job Piece 30373(07) Project segment from US-412A / State Highway 412A junction extending east 4.00 miles to State Highway 10 junction is 6,350 vehicles per day. By 2048, traffic is expected to grow to 7,950 vehicles per day.
For both the (04) and (07) projects 5% of the traffic is commercial trucks.

## Slide 6
Proposed Improvements
US-412A Open Section Reconstruction & Mill | Overlay with Shoulder Widening
One lane in each direction consisting of 12-foot-wide driving lanes
8-foot-wide paved shoulders
Design speed of 55 mph
US-412A | Reconstruction (Looking East)
US-412A | Mill / Overlay (Looking East)
Notes: Outside of the Town of Kansas US-412A will be widened to consist of two 12-foot driving lanes and 8-foot paved shoulders. In segments that require vertical or horizontal alignment corrections the entire roadway will be reconstructed. In sections that do not require an alignment correction the existing roadway will be milled and overlayed with shoulders widened to 8 feet. The design speed is 55 miles per hour.

## Slide 7
US-412A Open Section for Left | Right Turn Lanes at Leach School (Intersection of S 530 RD)
Mill | Overlay with Lane and Shoulder Widening
Proposed Improvements
Mill / Overlay with left turn lane
  Three 12-foot-wide driving lanes consisting of a westbound thru lane, eastbound left turn lane and eastbound thru lane
  2-foot-wide paved shoulders
  Design speed of 45 mph
US-412A | Mill / Overlay with Left Turn (Looking East)
US-412A | Mill / Overlay with Left and Right Turns (Looking East)
Mill / Overlay with left and right turn lanes
  Four 12-foot-wide driving lanes consisting of a westbound right turn lane, westbound thru lane, westbound left turn lane and eastbound thru lane
  2-foot-wide paved shoulders
  Design speed of 45 mph
Notes: At the intersection of US-412A and South 530 Road, US-412A will be widened to consist of a westbound thru lane, an eastbound left turn lane, and an eastbound thru lane on the west leg. The east leg will consist of a westbound right turn lane, a westbound thru lane, a westbound left turn lane, and an eastbound thru lane. The north leg of South 530 Road will consist of a northbound thru lane, a southbound thru lane, and a southbound left-hand turn lane. The south leg of South 530 Road will consist of a northbound thru lane and a southbound thru lane. Existing US-412A will be milled and overlayed along with lane and shoulder widened. South 530 Road will be realigned to the east to allow for new access to Leach School. The US-412A design speed is 45 miles per hour.

## Slide 8
US-412A Closed Section Reconstruction & Mill | Overlay with Curb and Sidewalk
Proposed Improvements
One lane is each direction consisting of 14-foot-wide driving lanes
6-inch-tall mountable curbs
4-foot-wide sidewalks
Design speed of 45 mph
US-412A | Reconstruction (Looking East)
US-412A | Mill / Overlay (Looking East)
Notes: Within the Town of Kansas, US-412A will be widened to consist of two 14-foot driving lanes, 6-inch-tall mountable curbs, and 4-foot-wide sidewalks. In segments that require vertical or horizontal alignment corrections the entire roadway will be reconstructed. In sections that do not require an alignment correction the existing roadway will be milled and overlayed with lanes widened to 14 feet. The design speed is 45 miles per hour.

## Slide 9
Bridge A: NBI 12931 (Saline Creek)
Proposed Improvements
3- 10’ x 5’ x 38’ long skewed bridge reinforced concrete box (RCB)
Extended upstream and downstream
32’ north from centerline of US-412A
32’ south from centerline of US-412A
Bridge A (Looking East)
Notes: Existing Bridge A is a triple cell 10-foot-wide by 5-foot-tall by 38-foot-long skewed bridge reinforced concrete box. Bridge A will be extended upstream 32 feet north of the US-412A centerline and downstream 32 feet south of the US-412A centerline. Saline Creek flows from north to south through the reinforced concrete box.

## Slide 10
Bridge B: NBI 12933 (Saline Creek)
Proposed Improvements
(10.5’ – 9’ – 10.5’) x 6’ x 34’ long bridge reinforced concrete box (RCB)
Extended upstream and downstream
30’– 7” north from centerline of US-412A
29’– 10” south from centerline of US-412A
Bridge B (Looking East)
Notes: Existing Bridge B is a triple cell 10.5-foot-wide by 9-foot-wide by 10.5-foot-wide by 6-foot-tall by 34-foot-long bridge reinforced concrete box. Bridge B will be extended upstream 29 feet and 10 inches south of the US-412A centerline and downstream 30 feet and 7 inches north of the US-412A centerline. Saline Creek flows from south to north through the reinforced concrete box.

## Slide 11
Bridge C: 12526 (Spring Creek)
Proposed Improvements
(10’ – 10’ – 8’ – 10’ – 10’) x 8’ x 30’ long bridge reinforced concrete box (RCB)
Extended upstream and downstream
28’ north from centerline of US-412A
28’ south from centerline of US-412A
Bridge C (Looking East)
Notes: Existing Bridge C is a quintuplet cell 10-foot-wide by 10-foot-wide by 8-foot-wide by 10-foot-wide by 10-foot-wide by 8-foot-tall by 30-foot-long bridge reinforced concrete box. Bridge C will be extended upstream 28 feet north of the US-412A centerline and downstream 28 feet south of the US-412A centerline. Spring Creek flows from north to south through the reinforced concrete box.

## Slide 12
Bridge D: 32782 (unnamed creek)
Proposed Improvements
Construct new bridge 2- 14’ x 10’ x 20’ long with 2’ drop into a 2- 14’ x 12’ x 97’ long skewed bridge reinforced concrete box (RCB)
57’– 9” north from centerline of US-412A
59’– 3” south from centerline of US-412A
Bridge D (Looking East)
Notes: The proposed new Bridge D is a double cell 14-foot-wide by 10-foot-tall by 20-foot-long with a 2-foot drop into a double cell 14-foot-wide by 12-foot-tall by 97-foot-long skewed bridge reinforced concrete box. The proposed extents will be from upstream 57 feet and 9 inches north of the US-412A centerline to downstream 59 feet and 3 inches south of the US-412A centerline. An unnamed creek flows from north to south through the reinforced concrete box.

## Slide 13
Proposed Right-of-Way & Public Utility Easement
Development of Construction Plans
Design development has advanced to include
  Highway / local roads
  Drainage
  Driveways
  Utility corridors
Proposed right-of-way and public utility easements for acquisition have been designed according to FHWA and ODOT guidelines
Public Utility Easement (PUE): An area within an owner’s property dedicated to the installation and use of public utility facilities.
Right-of-Way Acquisition Legend
Proposed Right-of-Way
Temporary Right-of-Way
Public Utility Easement
Notes: The design for the highway has advanced to the point where the proposed right-of-way and public utility easements can be determined. Right-of-way is property that ODOT will purchase to widen the highway. A public utility easement is an area within an owner’s property dedicated to the installation and use of public utility facilities. The design, to this point, includes the layout of the highway both horizontally and vertically, crossing drainage structures and driveways with side drains. The proposed right-of-way is shown with purple vertically hatched lines in the aerial on the screen. Public utility easements are shown with light blue dotted lines. Temporary right-of-way is shown in yellow dashed lines. Existing right-of-way is in dark blue and white hashed lines. The public meeting website includes an Interactive Map that shows the design and proposed right-of-way and easements for the entire project. You can use the Interactive Map to view your property. The public meeting website also includes additional information on the right-of-way purchase process.

## Slide 14
Project Overview with Map
Development of Construction Plans
Starts on US-412A south of the US-412A / US-412 junction
Continues east approximately 11.35 miles
  S 590 RD
  S 600 RD
  Cherokee St.
Includes Section Line Road intersections
  S 510 RD
  S 520 RD
  S 530 RD
  S 540 RD
Ends approximately 500 feet west of SH-10 intersection
  S 550 RD
  S 560 RD
  S 570 RD
  S 580 RD / SH-412A
Notes: The proposed improvements for US-412A will start south of the US-412A / US-412 junction and extend east approximately 11.35 miles to State Highway 10. Section Line Roads intersecting US-412A are South 510 Road, South 520 Road, South 530 Road, South 540 Road, South 550 Road, South 560 Road, South 570 Road, South 580 Road / State Highway 412A, South 590 Road, South 600 Road, and Cherokee Street. US-412A improvements will end approximately 500 feet west of the State Highway 10 intersection.

## Slide 15
Project Walk Through
Development of Construction Plans
Beginning of Project
  Begin project at the end of the existing 8-foot-wide shoulder section south of the US-412A / US-412 junction.
Intersection
  S 510 RD
Public utility easements are needed at two locations along the proposed right-of-way.
Temporary right-of-way is needed for one drainage channel west of S 510 RD.
Notes: The beginning of the project starts at the end of the existing 8-foot-wide shoulder section south of the US-412A / US-412 junction. South 510 Road intersects US-412A. Public utility easements are needed at two locations along the proposed right-of-way near South 510 Road. Temporary right-of-way is needed for one drainage channel west of South 510 Road.

## Slide 16
Project Walk Through
Development of Construction Plans
Intersection
  S 520 RD
Public utility easements are needed at three locations along the proposed right-of-way.
Temporary right-of-way is needed around three ponds near the intersection of S 520 RD and one drainage channel west of S 520 RD.
Temporary right-of-way is needed for two driveways west of S 520 RD.
Notes: South 520 Road intersects US-412A. Public utility easements are needed at three locations along the proposed right-of-way. Temporary right-of-way is needed around three ponds near the intersection of South 520 Road and one drainage channel west of South 520 Road. Temporary right-of-way is needed for two driveways west of South 520 Road.

## Slide 17
Project Walk Through
Development of Construction Plans
Intersection
  S 530 RD
Public utility easements are needed at three locations along the proposed right-of-way.
Temporary right-of-way is needed for Leach School access roads.
Notes: South 530 Road intersects US-412A. Public utility easements are needed at three locations along the proposed right-of-way. Temporary right-of-way is needed for Leach School access roads.

## Slide 18
Project Walk Through
Development of Construction Plans
Intersection
  S 540 RD
Public utility easements are needed at four locations along the proposed right-of-way.
Temporary right-of-way is needed for drainage channels around Bridges A and B west of S 540 RD and one drainage channel east of S 540 RD.
Notes: South 540 Road intersects US-412A. Public utility easements are needed at four locations along the proposed right-of-way. Temporary right-of-way is needed for drainage channels around Bridge A, Bridge B, and east of South 540 Road.

## Slide 19
Project Walk Through
Development of Construction Plans
Intersection
  S 550 RD
Public utility easements are needed at three locations along the proposed right-of-way.
Notes: South 550 Road intersects US-412A. Public utility easements are needed at three locations along the proposed right-of-way.

## Slide 20
Project Walk Through
Development of Construction Plans
Intersection
  S 560 RD
Public utility easements are needed at two locations along the proposed right-of-way.
Temporary right-of-way is needed for three drainage channels east of S 560 RD.
Notes: South 560 Road intersects US-412A. Public utility easements are needed at two locations along the proposed right-of-way. Temporary right-of-way is needed for three drainage channels east of South 560 Road.

## Slide 21
Project Walk Through
Development of Construction Plans
Intersections
  S 567 RD
  S 570 RD
Public utility easement is needed at one location along the proposed right-of-way.
Temporary right-of-way is needed for a drainage channel west of S 570 RD and a pond east of S 570 RD.
Notes: South 567 Road and South 570 Road intersect US-412A. A public utility easement is needed at one location along the proposed right-of-way. Temporary right-of-way is needed for drainage channels west of South 570 Road and a pond east of South 570 Road.

## Slide 22
Project Walk Through
Development of Construction Plans
Intersections
  S 580 RD / SH-412A
  S 584 RD
Public utility easements are needed at three locations along the proposed right-of-way.
Temporary right-of-way is needed for four driveways east of S 580 RD.
Notes: South 580 Road / State Highway 412A and South 584 Road intersect US-412A. Public utility easements are needed at two locations along the proposed right-of-way. Temporary right-of-way is needed for four driveways east of South 580 Road.

## Slide 23
Project Walk Through
Development of Construction Plans
Intersections
  S 588 RD
  S 590 RD
  S 593 RD
  S 594 RD
Public utility easements are needed at three locations along the proposed right-of-way.
Temporary right-of-way is needed for three drainage channels and one pond west of S 590 RD and one drainage channel east of S 590 RD.
Temporary right-of-way is needed for S 594 RD.
Notes: South 588 Road, South 590 Road, South 593 Road, and South 594 Road intersect US-412A. Public utility easements are needed at three locations along the proposed right-of-way. Temporary right-of-way is needed for three drainage channels and one pond west of South 590 Road and one drainage channel east of South 590 Road. Temporary right-of-way is needed for South 594 Road.

## Slide 24
Project Walk Through
Development of Construction Plans
Intersections
  S 596 RD
  S 600 RD
  S 601 RD
Public utility easements are needed at four locations along the proposed right-of-way.
Temporary right-of-way is needed for two drainage channels east of S 600 RD.
Temporary right-of-way is needed for S 594 RD and S 596 RD.
Notes: South 596 Road, South 600 Road, and South 601 Road intersect US-412A. Public utility easements are needed at four locations along the proposed right-of-way. Temporary right-of-way is needed for two drainage channels east of South 600 Road. Temporary right-of-way is needed for South 594 Road and South 596 Road.

## Slide 25
Project Walk Through
Development of Construction Plans
Intersections
  S 605 RD
  Woods Avenue
  Maple Lane
  Oak Street
Public utility easements are needed at four locations along the proposed right-of-way.
Temporary right-of-way is needed for Bridge C.
Temporary right-of-way is needed for two drainage channels west of Cherokee Street and two drainage channels east of Cherokee Street.
Temporary right-of-way is needed for one driveway west of Cherokee Street.
  Elm Street
  Cherokee Street
  Ezell Drive
Notes: South 605 Road, Woods Avenue, Maple Lane, Oak Street, Elm Street, Cherokee Street, and Ezell Drive intersect US-412A. Public utility easements are needed at four locations along the proposed right-of-way. Temporary right-of-way is needed for Bridge C. Temporary right-of-way is needed for two drainage channels west of Cherokee Street and two drainage channels east of Cherokee Street. Temporary right-of-way is needed for one driveway west of Cherokee Street.

## Slide 26
Project Walk Through
Development of Construction Plans
Intersections
  Mason Street
  Marianna Lane
Public utility easements are needed at two locations along the proposed right-of-way.
Ending of Project
  End project at approximately 500 feet west of the US-412A / SH-10 junction.
Notes: Mason Street and Marianna Lane intersect US-412A. Public utility easements are needed at two locations along the proposed right-of-way. The project ends approximately 500 feet west of State Highway 10.

## Slide 27
Geometric Corrections
Development of Construction Plans
Horizontal Curve Corrections
  30373(04): 1
Vertical Curve Corrections
  30373(04): 11
  30373(07): 18
Intersection Realignments
  30373(04): S 510 RD, S 570 RD
  30373(07): S 594 RD, S 596 RD, S 601 RD
Notes: The west project includes one horizontal curve correction at the intersection of South 510 Road. 29 vertical curves will be corrected throughout both projects. The projects include intersection realignments for South 510 Road, South 570 Road, South 594 Road, South 596 Road, and South 601 Road.

## Slide 28
Horizontal Curve Correction at S 510 RD Intersection
Development of Construction Plans
The horizontal curve will be realigned to meet current Federal Highway Administration (FHWA) and Oklahoma Department of Transportation (ODOT) design standards.
The US-412A and S 510 RD intersection will be realigned.
Notes: The US-412A horizontal curve near South 510 Road will be realigned to meet current Federal Highway Administration and Oklahoma Department of Transportation design standards. As a result, US-412A and South 510 Road intersection will be realigned.

## Slide 29
Plan View of New Vehicular Access to Leach School from S 530 RD and Realignment of S 530 RD
Development of Construction Plans
Intersection of US-412A and S 530 RD
  S 530 RD will be realigned to the east
  Left turn lane will be added to the west leg of US-412A
  Left and right turn lanes will be added to the east leg of US-412A
  Left turn lane will be added to the north leg of S 530 RD
A new loop access road will be added east of Leach School and connected to S 530 RD for bus pick up and drop off.
Access to the south parking lot will be maintained via the entrance off of S 530 RD.
The existing vehicular access between Leach School and US-412A will be removed.
Notes: The intersection of US-412A and South 530 Road will be realigned to the east. An eastbound left turn lane will be added to the west leg. A southbound left turn lane will be added to the north leg. Westbound left and right turn lanes will be added to the east leg. A new loop access road will be added along the east side of Leach School and connected to South 530 Road for bus pick up and drop off. Access to the south parking lot will be maintained via the entrance off South 530 Road. The existing vehicular access between Leach School and US-412A will be removed.

## Slide 30
National Environmental Policy Act (NEPA)
Environmental
A NEPA document will be prepared for Federal Highway Administration approval.
Commitments to avoid and/or minimize impacts to the environment will be included in the project in accordance with the NEPA.
ODOT Completed Studies
Cultural Resources (Historic and Archeological)
Waters and Wetlands
Threatened and Endangered Species
Hazardous Materials Assessment
Floodplains
Assessment
Notes: A National Environmental Policy Act document will be prepared for Federal Highway Administration approval.
ODOT has completed studies for:
Cultural Resources (Historic and Archeological)
Waters and Wetlands
Threatened and Endangered Species
Hazardous Materials Assessment
Floodplains Assessment
Commitments to avoid and/or minimize impacts to the environment will be included in the project in accordance with the National Environmental Policy Act.

## Slide 31
Gray Bat, Neosho Mucket, American Burying Beetle, Piping Plover, Red Knot, Indiana Bat, Rabbitsfoot Mussel, Monarch Butterfly
Environmental Studies
Threatened and Endangered Species
The project area includes habitat for several protected species, including several bat and mussel species as well as the American Burying Beetle.
Measures to minimize or avoid impacts to these species will be added to the project plans.
These measures may include performing additional surveys, seasonal restriction on tree clearing, and requirements for project lighting.
Notes: The project area includes habitat for several protected species, including several bat and mussel species as well as the American Burying Beetle. Measures to minimize or avoid impacts to these species will be added to the project plans. These measures may include performing additional surveys, seasonal restriction on tree clearing, and requirements for project lighting.
The endangered species located within Delaware County include the Gray Bat, Neosho Mucket, American Burying Beetle, Piping Plover, Red Knot, Indiana Bat, Rabbitsfoot Mussel and
Monarch Butterfly.

## Slide 32
Environmental Studies
Waters & Wetlands
The project may have impacts to waters and/or wetlands regulated by the U.S. Army Corps of Engineers.
If required, ODOT will obtain the appropriate Clean Water Act permit prior to construction.
The contractor will employ best management practices to prevent erosion and keep sediment and other hazardous materials out of streams.
Notes: The project may have impacts to waters and/or wetlands regulated by the US Army Corps of Engineers. If required, ODOT will obtain the appropriate Clean Water Act permit prior to construction. The contractor will employ best management practices to prevent erosion and keep sediment and other hazardous materials out of streams.

## Slide 33
Environmental Studies
Cultural Resources
The project will not have impacts to any significant historic or archeological sites.
A Built Environment Historic Resources Survey was completed that documented 3 buildings and 29 building complexes. In all, 76 historic age (built in or before 1977) resources were documented. These resources within the study area are not historically significant and/or they do not retain adequate historic and physical integrity to convey their historic significance. Therefore, all surveyed resources of the built environment are recommended as not eligible for NRHP listing.
To avoid non-NRHP assessed cultural resources and cemeteries during off-project activities such as fill borrowing, areas have been recommended for avoidance.
Notes: The project will not have impacts to any significant historic or archeological sites.
A Built Environment Historic Resources Survey was completed that documented 3 buildings and 29 building complexes. In all, 76 historic age (built in or before 1977) resources were documented. These resources within the study area are not historically significant and/or that they do not retain adequate historic and physical integrity to convey their historic significance. Therefore, all surveyed resources of the built environment are recommended not eligible for NRHP listing.
To avoid non-NRHP assessed cultural resources and cemeteries during off-project activities such as fill borrowing, areas have been recommended for avoidance.

## Slide 34
Hazardous Materials
A review of known contaminated sites in the project area revealed fifteen (15) current or former petroleum storage tank locations along the project corridor. Plan notes for potential issues may be added to the project plans.
Environmental Studies
Notes: A review of known contaminated sites in the project area revealed fifteen (15) current or former petroleum storage tank locations along the project corridor. Plan notes for potential issues may be added to the project plans.

## Slide 35
Environmental Studies
Floodplains
The project will not involve an increase to the base 100-year floodplain in a regulatory floodway (Zone A in a FEMA Map) that will require a flood map revision.
Zone A
Zone A
Zone A
Zone A
Notes:   The project will not involve an increase to the base 100-year floodplain in a regulatory floodway (Zone A in a FEMA Map) that will require a flood map revision.

## Slide 36
Estimated Relocations
To Accommodate Highway Widening Additional Right-of-Way will be Required
ODOT took steps to minimize relocations by using a public utility easement (PUE) along the proposed project, rather than acquiring additional right-of-way to move utilities.
No other measures can be taken to mitigate displacements, while accomplishing the purpose of the proposed project (adding 8-foot-wide paved shoulders), due to the proximity of the structures to the roadway.
Estimated relocations for the 11.35-mile project include:
  26 residential properties
  14 commercial properties
  2 non-residential and non-commercial (Timber Grove Free Holiness Church and Kansas Public Library)
The parcels on which most of the displaced residential properties are located include enough space to relocate the displaced structures on the same property; however, should the residents/owners be unable to relocate within the same parcel of land, the lack of comparable replacement properties in the immediate vicinity may require construction of new structures, potentially delaying or extending the proposed project timeline.
Right-of-Way Acquisition is expected to start in Spring 2024.
Notes: To accommodate the US 412A highway widening, additional Right of Way will be required.
ODOT took steps to minimize relocations by using a public utility easement (PUE) along the proposed project, rather than acquiring additional right-of-way to move utilities. No other measures can be taken to mitigate displacements, while accomplishing the purpose of the proposed project for adding 8-foot-wide paved shoulders, due to the proximity of the structures to the roadway.
Estimated relocations using the PUE for the 11.35-mile project include:
26 residential properties
14 commercial properties
2 non-residential and non-commercial (Timber Grove Free Holiness Church and Kansas Public Library)
The parcels on which most of the displaced residential properties are located include enough space to relocate the displaced structures on the same property; however, should the residents/owners be unable to relocate within the same parcel of land, the lack of comparable replacement properties in the immediate vicinity may require construction of new structures, potentially delaying or extending the proposed project timeline. Right-of-Way Acquisition is expected to start in Spring of 2024.

## Slide 37
Estimated Relocations
To Accommodate Highway Widening Additional Right-of-Way will be Required
Any properties being impacted by the proposed right-of-way acquisition on this project may be entitled to relocation benefits. The eligibility of each property impacted will be determined through the right-of-way process. Acquisition and relocation assistance will be conducted in accordance with the Uniform Relocation Assistance and Real Property Acquisitions Act of 1970, as amended effective February 3, 2005.
Without using the public utility easements, the original relocation estimates are noted below (January 2021):
  37 residential properties
  22 commercial properties
Estimated relocations have been REDUCED by the following numbers by use of the public utility easements:
  11 residential properties
  8 commercial properties
Right-of-Way Acquisition is expected to start in Spring 2024.
Notes: Any properties being impacted by the proposed right-of-way acquisition on this project may be entitled to relocation benefits. The eligibility of each property impacted will be determined through the right-of-way process. Acquisition and relocation assistance will be conducted in accordance with the Uniform Relocation Assistance and Real Property Acquisitions Act of 1970, as amended effective February 3, 2005.
Without using the public utility easements, the original relocation estimates are noted below:
37 residential properties
22 commercial properties
Estimated relocations have been REDUCED by the following numbers by use of the public utility easements:
11 residential properties
8 commercial properties

## Slide 38
Estimated Relocations
To Accommodate Highway Widening Additional Right-of-Way will be Required
Please use the following links to view the ODOT Property Rights Brochure and the ODOT Relocation Brochure.
ODOT Relocation Brochure
ODOT Property Rights Brochure
Right-of-Way Acquisition is expected to start in Spring 2024.
Notes: Please use the links below to view the ODOT Property Rights Brochure and the ODOT Relocation Brochure
Again, Right-of-Way Acquisition is expected to start in the Spring of 2024. Starting in the Spring, property owners will be contacted by a right-of-way acquisition agent who will assist in the acquisition process with each property owner.

## Slide 39
Construction
Construction Plan
Construction is currently in the ODOT 8-year CONSTRUCTION PROJECT plan to begin in Fiscal Year 2027 & 2028
PROJECT WILL BE CONSTRUCTED IN PHASES
TRAFFIC WILL BE MAINTAINED THROUGHOUT CONSTRUCTION
Access will be maintained to all residences and businesses during construction
Notes: Construction of US-412A from the US-412A / US-412 Junction to State Highway 10 is currently scheduled in the Oklahoma Department of Transportation 8-year construction project plan to begin in fiscal year 2027 for Job Piece 30373(04) and fiscal year 2028 for Job Piece 30373(07).
Project will be constructed in phases.
US-412A will remain open during construction. Access from US-412A will be maintained to all homes and businesses during construction.

## Slide 40
Today
Next Steps
Project Schedule
August 17, 2023
Spring 2024
FFY 2028
Fall 2023
FFY 2027
Public Comments Due
Environmental NEPA Document
Start Right-of-Way Acquisition
30373(04)
Programmed for Construction
30373(07) Programmed for Construction
Notes: We ask that you submit your comments by August 17, 2023 so that we may incorporate your feedback and finalize the design plans.
Federal Highway Administration approval for the Environmental National Policy Act Document is anticipated in Fall 2023.
If your property is affected by the project, you can expect to hear from ODOT right-of-way agents beginning in Spring 2024.
Current construction of the Job Piece 30373(04) project is programmed to begin in fiscal year 2027. The Job Piece 30373(07) project is programmed to begin in fiscal year 2028.

## Slide 41
THANK YOU!
We appreciate your participation in our Virtual Open House Public Meeting!
Please visit the following areas on the ODOT website for more information.
INTERACTIVE MAP
View the design on the aerial photograph, zoom in and out, find your property, etc.
RIGHT-OF-WAY ACQUISITION
Information for right-of-way acquisition and relocations.
FREQUENTLY ASKED QUESTIONS
Common questions and answers about the project.
SUBMIT A COMMENT
Submit your comments or questions on this page or send by email or U.S. mail.
Submit a written comment or question to “Submit a Comment” page on the ODOT website www.odot.org/US412ADelaware
Comments or Questions
Send an Email to environment@odot.org.
For more information, please call 405-325-3269.
41
Notes: Thank you for participating in the Virtual Open House Public Meeting!
Please visit the following areas on the ODOT website for more information regarding the interactive map, right-of-way acquisition, frequently asked questions, and to submit a comment. Use the interactive map to view the design on the aerial photograph, zoom in and out, find your property, etc. Find information about right-of-way acquisitions and relocations. See frequently asked questions and answers about the project. Submit your comments or questions through the website, email, or U.S. mail.
If you have comments or questions please submit a written comment or question to “Submit a Comment” page on the ODOT website www.odot.org/US412ADelaware or send an email to environment@odot.org. For more information, please call 405-325-3269.
This concludes the meeting presentation.