## Slide 1: EDC-2 INTERSECTION AND INTERCHANGE DESIGN
DIVERGING DIAMOND INTERCHANGE – DDI
SINGLE POINT URBAN INTERCHANGE – SPUI
ROUNDABOUTS
Displaced left turns: jturns, rcuts - reduced conflict u-turns

## Slide 2: DIVERGING DIAMOND INTERCHANGE
SH-6 over I-40
ELK CITY, OKLAHOMA
BECKHAM COUNTY

## Slide 3: LOCATION: Beckham County, Elk City, Oklahoma: SH-6 over Interstate 40 FEDERAL AID PROJECT NO.: ACNHPPI-4000-(061) PM STATE JOB NO.: 30998(04) CONTROL SECTION: 06-05-14 BRIDGE “A” LOCATION NO.: 0504-1378X NEW NBI NO.: 31995 OLD NBI NOS.: 17557 & 17558 BRIDGE LENGTH: 283.66’ CONTRACTOR: FRONTIER BRIDGE
Project Information:

## Slide 4
Elk City DDI: Satellite Imagery

## Slide 5
OLD BRIDGES IN 2017
SH-6 over I-40

## Slide 6: OLD BRIDGES in 2017 I-40 WB under SH-6

## Slide 7: OPERATIONAL PERFORMANCE
The traffic simulation software VISSIM was used to compare the operational performance of a typical Diverging Diamond Interchange to conventional diamond interchanges.
Demonstrated:
Less Delays
Fewer Stops
Reduced Stop Times
Shorter Queue Lengths
Delays were reduced by 15 to 60 percent
Throughput was increased by 10 to 30 percent

## Slide 8: Phase I Construction July 2019

## Slide 9: Phase I Construction July 2019

## Slide 10: SAFETY
31 Collisions between 2011 and 2015
45% Rear-End
32% Right-Angle
19% Angle Turning
No Reported Accidents Since Full Operation
Some research has shown a 63% reduction in serious crashes and a 41% reduction in overall crashes when converting a conventional diamond interchange to a DDI.

## Slide 11: Phase I Construction July 2019

## Slide 12: Phase I Construction July 2019

## Slide 13: Phase I Construction August 2019

## Slide 14: Phase I Construction August 2019

## Slide 15: Phase I Construction August 2019

## Slide 16: Phase I Construction August 2019

## Slide 17: Phase I Construction August 2019

## Slide 18: Phase I Construction August 2019

## Slide 19: Phase I Construction August 2019

## Slide 20: Phase I Construction September 2019

## Slide 21: Phase I Construction September 2019

## Slide 22: Phase I Construction September 2019

## Slide 23: Phase I Construction September 2019

## Slide 24: Phase I Construction September 2019

## Slide 25: Phase I Construction September 2019

## Slide 26: Phase I Construction October 2019

## Slide 27: Phase I Construction October 2019

## Slide 28: Phase I Construction October 2019

## Slide 29: Phase I Construction October 2019

## Slide 30: Phase I Construction October 2019

## Slide 31: Phase I Construction November 2019

## Slide 32: Phase I Construction November 2019

## Slide 33: Phase I Construction November 2019

## Slide 34: Phase I Construction November 2019

## Slide 35: Phase I Construction November 2019

## Slide 36: Phase I Construction November 2019

## Slide 37: Phase I Construction December 2019

## Slide 38: Phase I Construction December 2019

## Slide 39: Phase I Construction December 2019

## Slide 40: Phase I Construction December 2019

## Slide 41: Phase II Construction February 2020

## Slide 42: Phase II Construction February 2020

## Slide 43: Phase II Construction February 2020

## Slide 44: Phase II Construction February 2020

## Slide 45: Phase II Construction June 2020

## Slide 46: Phase II Construction June 2020

## Slide 47: Phase II Construction june 2020

## Slide 48: Phase II Construction june 2020

## Slide 49: Phase II Construction june 2020

## Slide 50: Phase II Construction june 2020

## Slide 51: Phase II Construction june 2020

## Slide 52: Phase II Construction june 2020

## Slide 53: Phase II Construction june 2020

## Slide 54: Phase II Construction October 2020

## Slide 55: Phase II Construction October 2020

## Slide 56: Phase II Construction October 2020

## Slide 57: Phase II Construction October 2020

## Slide 58: Phase II Construction October 2020

## Slide 59: Phase II Construction October 2020

## Slide 60: Completed Project March 2021

## Slide 61: Completed Project March 2021

## Slide 62: Completed Project March 2021

## Slide 63: Completed Project March 2021

## Slide 64: Completed Project March 2021

## Slide 65: Completed Project March 2021

## Slide 66: Completed Project March 2021

## Slide 67: Future Projects Waterloo Road under I-35 Oklahoma County

## Slide 68: Future Projects I-35 over Waterloo Road Oklahoma County

## Slide 69: Future Projects US-64 under US-169 Tulsa County

## Slide 70: Future Projects US-64 under US-169 Tulsa County

## Slide 71: INTERSECTION & INTERCHANGE GEOMETRICS
About half of all severe crashes in the U.S. are intersection related. Left-turns represent a large portion of the intersection safety concern. As part of the safety focus area of the Every Day Counts (EDC) initiative, the Federal Highway Administration (FHWA) is promoting several proven techniques to improve the safety of intersections by strategically eliminating or relocating the left-turn conflicts. Transportation agencies that apply the intersection and interchange geometrics under this initiative can reduce crashes and greatly enhance the efficiency of moving traffic, often times with substantial cost savings and accelerated project delivery.

## Slide 72: INTERSECTION & INTERCHANGE GEOMETRICS
Single Point Urban Interchange – SPUI: This design allows a large volume of vehicles to travel through an intersection safely and efficiently by reducing the number of conflict points and the number of traffic signal phases. Like the Diverging Diamond Interchange, it allows opposing left turns to proceed simultaneously. Opposing left turns can be made at the same time with only one set of traffic signals, allowing more vehicles to clear the intersection in one traffic signal cycle. The SPUI improves travel times, provides wider turns for larger vehicles, and reduces Right-of-Way requirements.

## Slide 73: Single Point Urban Interchanges – SPUI: I-40 and Morgan Rd. OKC

## Slide 74: Single Point Urban Interchanges – SPUI: I-40 and Morgan Rd. OKC

## Slide 75: Single Point Urban Interchanges – SPUI: I-35 and Main ST. Norman

## Slide 76: Single Point Urban Interchanges – SPUI: I-35 and Main St. Norman

## Slide 77: Single Point Urban Interchanges – SPUI: I-35 and Lindsey St. Norman

## Slide 78: Single Point Urban Interchanges – SPUI: I-35 and Lindsey St. Norman

## Slide 79: INTERSECTION & INTERCHANGE GEOMETRICS
Roundabouts: Modern roundabouts have proven results for reducing severe crashes and they are a very adaptable intersection geometry. Roundabouts have been successfully deployed across a wide range of contexts including at isolated rural intersections with high approach speeds and in intensely developed urban settings that include extensive pedestrian and bicycle features. Furthermore, in certain environments with constrained right-of-way, the application of mini-roundabouts is gaining acceptance. Mini-roundabouts typically feature a fully traversable central island.

## Slide 80: Roundabouts – I-35 Frontage Rd. Goldsby Exit

## Slide 81: Roundabouts – I-35 Frontage Rd. Goldsby Exit

## Slide 82: Roundabouts – I-35 Frontage Rd. Goldsby Exit

## Slide 83: Roundabouts – Price Rd. Bartlesville

## Slide 84: Roundabouts – NW 59th OKC

## Slide 85: Traffic Calming Roundabout – Midwest City

## Slide 86: INTERSECTION & INTERCHANGE GEOMETRICS
U-Turn Intersections (Restricted Crossing U-Turns, J-Turns, Median U-Turns, and ThrU-Turns): These intersection geometries involve related strategies for modifying some traffic movements at the primary intersection with a U-turn movement. Variations of this strategy are appropriate for a wide range of conditions, including unsignalized rural intersections and high volume signalized arterials.

## Slide 87: Restricted Crossing U-Turns (RCUT): US-75 Washington Co.

## Slide 88: Restricted Crossing U-Turns (RCUT): US-75 Washington Co.

## Slide 89: Restricted Crossing U-Turns (RCUT): US-75 Washington Co.

## Slide 90: Restricted Crossing U-Turns (RCUT): US-75 Washington Co.