## Slide 1: Every Day Counts so OK up (Safe Transportation for Every Pedestrian) OK STIC EDC-4 STEP Webinar July 13, 2022

## Slide 2: The numbers in 2017 when STEP initiated
2
Pedestrians now account for a larger proportion of traffic fatalities (16%) than they have in the past 33 years
Photo Credit: GHSA

## Slide 3: The numbers from the latest GHSA Report

## Slide 4
Why STEP?
Over 72% of pedestrian fatalities occur at non-intersection locations (mid-block)
Roughly 27% of pedestrian fatalities occur at intersections (with more at uncontrolled)
4

## Slide 5
Crosswalk Visibility Enhancements
Raised Crosswalks
Pedestrian Refuge Island
Rectangular Rapid Flashing Beacon (RRFB)
Pedestrian Hybrid Beacon (PHB)
Road Diets
Leading Pedestrian Interval (LPI)
The Fabulous Five to Spectacular Seven

## Slide 6
Crosswalk Visibility Enhancements
High Visibility Marked Crosswalks
Signing and Markings
Lighting
Curb Extensions / Bulb Outs
Parking Restrictions
Curb Radius

## Slide 8
Two or three lanes
Speed limits of 30 mph or less
AADT below 9,000

## Slide 11
https://sahuaritaaz.gov/DocumentCenter/View/5621/Sah_bill-insert_Summer-2020_web?bidId=
Notes: Town of Sahuarita AZ
Bullet Points from Richard Nassi
Speed Limit 45mph
  85th Percentile guesstimated at least 50 mph.
Observed for about an hour
  Driver compliance 100%.
Installation cost $26,000.
Device manufactured in Phoenix.
Very effective

## Slide 13
General Guidelines for Traffic Volumes
In most instances traffic will likely not be negatively affected.
Agencies should conduct intersection analysis to study potential traffic operational effects and consider signal retiming as needed.
Agencies should conduct a corridor analysis since traffic operations may be affected at this volume depending on the “before” condition.
LESS THAN
10,000 ADT
10,000 – 15,000 ADT
Great candidate for Road Diet
15,000 – 20,000 ADT
Agencies should complete a feasibility study to determine whether this is a good location for a Road Diet. Operations may be affected at this volume.
GREATER THAN
20,000 ADT
Very good candidate for Road Diet
Good candidate for Road Diet
Potential candidate for Road Diet
There are examples across the country where Road Diets have been successful with ADTs as high as 26,000

## Slide 14
2005
2018

## Slide 16: Guide for Improving Pedestrian Safety at Uncontrolled Crossing Locations
www.fhwa.dot.gov/innovation/everydaycounts/edc_4/guide_to_improve_uncontrolled_crossings.pdf

## Slide 18: FHWA STEP Website https://safety.fhwa.dot.gov/ped_bike/step/resources/

## Slide 19
The Safe System Approach
Source: FHWA
19
Zero is our Goal. a Safe System is how we get there

## Slide 20: Now Live: FHWA CS Web Portal
Public facing web-portal to:
  Publish all Complete Streets products
  Link to CS resources across FHWA program offices and other stakeholders
https://highways.dot.gov/complete-streets
20

## Slide 21: Safe Streets and Roads for All (SS4A) Grant Program
Funds regional, local and Tribal initiatives to prevent roadway deaths and serious injuries
$5 billion in appropriated funds over the next 5 years. In fiscal year 2022 (FY22), up to $1 billion is available.
The SS4A program funds regional, local, and Tribal initiatives through grants to prevent roadway deaths and serious injuries.
Visit www.transportation.gov/SS4A to:
Find resources, FAQs and application information
Applications are due September 15, 2022 5 pm EDT

## Slide 22: Taken at my first STEP Workshop in Claremore OK

## Slide 23: Oklahoma DOT Piloting and training on STEP countermeasures
Shelby Templin
ODOT Active Transportation Coordinator

## Slide 24: STEP Workshops
Safe Transportation for Every Pedestrian Workshops
  3 classes held November 2017
  Coordination between FHWA, ODOT and Oklahoma LTAP
  Each class included classroom instruction (Peter Eun), field examinations, and site analysis

## Slide 25: STEP Workshops
Classroom Learning – Lawton Class

## Slide 26: STEP Workshops
Site examination and field observation – Edmond Class

## Slide 27: STEP Workshops
Site analysis and countermeasure proposal – Claremore Class

## Slide 28: Countermeasures and options
Current considered options and treatments
  Road Diets
  Pedestrian Hybrid Beacons
  Pedestrian Refuge Islands
  Raised Crosswalks
  Crosswalk Visibility Enhancements
Education is key
Must know what treatments are appropriate for individual locations

## Slide 29: STEP Plan development
State of Oklahoma STEP Plan
  Plan development session held at ACOG offices on Nov. 30, 2017
  Representatives from ODOT, ACOG, INCOG, OHSO, FHWA and the Seminole Nation attended
  Draft STEP Plan developed through discussions between group at brainstorming session
  Several ODOT divisions reviewed the plan document and made decisions for the policy guidance based on the countermeasures discussed

## Slide 30: STEP Plan development
Finalization and distribution end of 2018
Copies sent to all Divisions and Field Districts
Countermeasures are now encouraged, when applicable

## Slide 31: STEP Plan: Next “Steps”
Buy in from ODOT Divisions, FHWA Oklahoma, MPOs, RTPOs, ADA Development, etc
Increased awareness about Pedestrian Safety to the general public
Continue to encourage countermeasures, where appropriate
Stay up to date when countermeasures are being integrated into plan design

## Slide 32: Placemaking with Road Diets in oklahoma
https://vimeo.com/277314570